## Slide 1
Space Syntax Toolkit for QGIS Introduction and recent developments
Jorge Gil
Stephen Law
Ioanna Kolovou
Abhimanyu Acharya
Space Syntax Laboratory - UCL
Space Syntax Limited - Open Digital Works
11th International Space Syntax Symposium
Fundação Calouste Gulbenkian, Lisbon
3rd July 2017

## Slide 2
Introduction
Who we are
Jorge Gil MSc, PhD
Researcher UCL, Chalmers, TU Delft
Open Source GIS consultant and developer
Author ‘Space Syntax Toolkit’ for QGIS (2013 - )
Author ‘Confeego’ for MapInfo (2004 - 09)
Stephen Law MSc, PhD
Researcher Turing Institute, UCL
Associate, Space Syntax Limited
Ioanna Kolovou MRes
Consultant, Space Syntax Limited
Abhimanyu Acharya MSc
Associate, Space Syntax Limited

## Slide 3
Introduction

## Slide 4
Introduction
Who are you?
Name and affiliation

## Slide 5
Introduction
Who are you?
 | Yes / Some | No
space syntax | 5 | 1
depthmapX | 4 | 2
QGIS | 1 | 5
GIS | 3 | 2
Note: based on 6 participant’s responses.

## Slide 6
Introduction
Objectives
Learn how to use the 'Space Syntax Toolkit' (SST) for QGIS
Learn about its latest features and tools
Explore various space syntax analysis workflows in QGIS
Main objective is not to…
Learn about space syntax theory and methods
Learn about the depthmapX software
Learn about specific space syntax applications in research

## Slide 7
Requirements
Participants must bring their own laptops in order to carry out the practical exercises, with the necessary software pre-installed:
QGIS 2.14 LTR (or higher):
http://qgis.org/en/site/forusers/download.html
depthmapXnet 0.35:
http://archtech.gr/varoudis/depthmapX/?dir=depthmapXnet
Space Syntax Toolkit:
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit/wiki/Installation
Introduction

## Slide 8
Programme
09:30 Introduction to the workshop
09:45 Overview of space syntax and the SST project
10:00 Task 1: Preparing and analysing axial models
11:00 Break
11:45 Task 2: Preparing and analysing road centre line models
12:30 Visualisation and discussion of the results
13:00 Lunch Break
14:00 Task 3: Preparing other urban data layers
15:00 Task 4: Connecting and analysing the various results
16:00 Discussion on QGIS methods for space syntax research
16:30 Close
Introduction

## Slide 9
Space syntax theory and the SST project
Overview of relevant space syntax concepts
Overview of the SST project
SST installation in QGIS and downloading the sample data set
Overview

## Slide 10
Relevant space syntax concepts
Representing space: axial maps and unlinks
Topology of space: graphs and centrality analysis
Segment maps and angular centrality analysis
Radius and distances
Space syntax theory

## Slide 11
Representing space: axial maps and unlinks
The axial map is a linear representation of space, with the fewest longest set of straight lines that covers all spaces.
Space syntax theory
Source: Hillier, B., Hanson, J., 1984. The Social Logic of Space. Cambridge University Press, Cambridge, UK

## Slide 12
Representing space: axial maps and unlinks
The axial map is a linear representation of space, with the fewest longest set of straight lines that covers all spaces.
Space syntax theory
Unlinks are features that mark a location where the intersection between two axial lines does not allow a change of direction.
Source: Hillier, B., Hanson, J., 1984. The Social Logic of Space. Cambridge University Press, Cambridge, UK

## Slide 13
Topology of space: graphs and centrality analysis
Axial maps are translated into mathematical graphs where every line represents a node, and every intersection between lines represents an edge, or link.
Where there is an unlink, no edge is created, because there is no intersection.
Space syntax theory

## Slide 14
Topology of space: graphs and centrality analysis
Space syntax theory
Connectivity
(Degree centrality)
Number of connected nodes
Mean Depth  Integration
(Closeness centrality)
Average distance to all other nodes
Choice
(Betweenness centrality)
Number of times on the shortest path
Between pairs of nodes

## Slide 15
Topology of space: graphs and centrality analysis
Space syntax theory
Source: Al-Sayed, K., Turner, A., Hillier, B., Iida, S., Penn, A., 2015. Space Syntax methodology. Bartlett School of Architecture, UCL, London.

## Slide 16
Segment maps and angular analysis
The segment map is the result of a transformation of the axial map, where the lines are broken at every intersection:
to obtain a more fin-grained result along axial lines;
Space syntax theory

## Slide 17
Segment maps and angular analysis
The segment map is the result of a transformation of the axial map, where the lines are broken at every intersection:
to obtain a more fin-grained result along axial lines;
to allow the measurement of the different angles of intersection along a route.
Space syntax theory

## Slide 18
Radius and distances
The graph analysis can be carried out for distances to all nodes in the graph, or just to nodes within a certain distance. This cut-off point is called the RADIUS of analysis.
To all nodes the radius is called ‘Radius N’
The distance used to calculate the shortest paths or determine the radius can vary, depending on the model being analysed:
Axial analysis: distance is always Topological, for paths and radius.
e.g. Axial Integration R3, or Axial Choice RN
Segment analysis: distance can be topological, metric or angular. BUT the standard in space syntax research is, Angular path distance, with Metric radius distance.
e.g. Segment Angular Choice R800m
Space syntax theory

## Slide 19
Overview of the project
An open source project for space syntax education, research and practice
Initiated by the Space Syntax Laboratory, UCL
For the space syntax community
WITH contributions from the space syntax community
Aims of the project
Integrate space syntax spatial analysis (depthmapX) with QGIS
User friendly for students: clear and linear workflows
Flexible for researchers: analytic options and exploratory depth
Operational for practice: robust, fast and optimised workflows
The SST Project

## Slide 20
The SST Project

## Slide 21
The SST Project

## Slide 22
SST Installation

## Slide 23
SST Installation

## Slide 24
SST sample data
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit/releases

## Slide 25
Original tools: SST version 0.1.x
Graph Analysis
Attribute Explorer

## Slide 26
New Set of tools: SST version 0.2.0
Catchment Analyser
Urban Data Input Tool
Road network cleaner
Gate Transformer

## Slide 27
Demo Workflow
RCL Topology Cleaning
Processing algorithm: simplify geometries
Space Syntax Analysis
Catchment Analyser
Visualisation
Gate Transformer/movement correlation
Urban data input
Integrated Urban Model
Axial Map Verification
Unlinks Verification

## Slide 28
Preparing and analysing axial models
Model preparation: making axial and unlinks maps
Model verification: verifying the axial and unlinks maps
Model analysis: Axial and segment analysis of the axial model
Visualising the results
Task 1

## Slide 29
Model preparation: making axial and unlinks maps
Preparing and analysing axial models

## Slide 30
Model verification: verifying the axial and unlinks maps
Preparing and analysing axial models

## Slide 31
Model analysis: Axial analysis of the axial model
Preparing and analysing axial models

## Slide 32
Model analysis: Segment analysis of the axial model
Preparing and analysing axial models

## Slide 33
Visualising the results
Preparing and analysing axial models

## Slide 35
Preparing and analysing road centre line (RCL) models
Comparing RCL maps
Cleaning RCL maps
Simplifying RCL maps
Verifying RCL maps
Analysing RCL maps
Task 2

## Slide 36
Comparing Road Centre Line maps
OpenStreetMap
OS Open Roads
OS Meridian 2

## Slide 37
This plugin corrects topological errors of Road-centre-line (RCL) maps. This is a necessary step before performing space syntax analysis to any network.
Cleaning RCL maps: Road network cleaner tool

## Slide 38
Road network cleaner
Removes invalid geometries
Removes point geometries
Breaks multi-part geometries
Breaks geometries at self intersection (1), at shared vertices (2) and where they touch endpoints of other lines (3).
Merges lines between intersections
Removes duplicate and overlapping (1) geometries, closed polylines that do not connect to any other line (2) and isolated lines (3).
Geometry
Topology
x
x
x

## Slide 39
Road network cleaner
Input layer Choose RCL map to clean. The input can be any QGIS layer.
Snap endpoints The user can specify a decimal precision of the coordinates
Output layers The user can choose between a memory QGIS layer a shapefile or a PostGIS database layer.
Load error layer The errors that have been corrected by the plugin can be loaded as a memory layer.
Load unlinks layer There is an option to create a memory unlinks layer where the lines of the input layer cross. However, unlinks should be verified by the user as RCL may represent differently unlinked lines.
Info See which topological errors are corrected.
Run Pressing run will perform the cleaning of the selected map
Cancel Pressing close will close and terminate the Road network cleaner

## Slide 40
Road network cleaner
Shapefile
Save output file: Select the location you wish to save the cleaned shapefile.
PostGIS layer
Database Select the database where to save the cleaned layer
Schema Select the schema where to save the cleaned layer
Table name Specify the table name of the cleaned layer or leave it as default (‘cleaned’)

## Slide 41
Cleaning RCL maps
OpenStreetMap
input
OS Open Roads
input

## Slide 42
Cleaning RCL maps
OpenStreetMap
errors
OS Open Roads
errors

## Slide 43
Cleaning RCL maps
OpenStreetMap
output
OS Open Roads
output

## Slide 44
Simplifying RCL maps
Source: https://www.researchgate.net/figure/260758647_fig6_Figure-6-Simplification-of-a-polygonal-curve-with-the-Douglas-Peucker-algorithm-A
Douglas-Peucker generalisation algorithm

## Slide 45
Simplifying RCL maps
QGIS – Simplify geometries

## Slide 46
Simplifying RCL maps
OpenStreetMap
OS Open Roads
Simplification threshold 10
Simplification threshold 10

## Slide 47
Simplifying RCL maps
OpenStreetMap
OS Open Roads
Simplification threshold 20
Simplification threshold 20

## Slide 48
Simplifying RCL maps
OS Meridian 2
OS Open Roads
No simplification
Simplification threshold 20

## Slide 49
Simplifying RCL maps
OpenStreetMap – threshold 20
OpenStreetMap
Simplification threshold 20
No simplification

## Slide 50
Verifying RCL maps
Graph Analysis tool
Unlinks
Verify the unlinks: This is required in the cases where the cleaning tool produces a meaningful unlinks result file, e.g. OS OpenRoads and OS Meridian2.

## Slide 51
Analysing RCL maps
Graph Analysis tool
Map
Segment map or road centre line: Tick this option when you are analysing road centre line maps or axial maps already segmented.

## Slide 52
Analysing RCL maps
OpenStreetMap
OS Open Roads
Integration RN, 10 equal ranges
Integration RN, 10 equal ranges

## Slide 54
Preparing other urban data layers
Urban Data Input Tool: recoding frontages, entrances and land use surveys
Creating the data layer
Drawing new features
Updating features
Viewing the attributes
Task 3

## Slide 55
Urban Data Input Tool
Urban Data Input Tool is a plugin to ease aid the input of urban data like frontage type, entrance type and land use type as per Space Syntax Limited standards. The Space Syntax community is the key users for the plugin. The display styles and categories included are as per Space Syntax Limited Standards.

## Slide 56
Urban Data Input Tool
Entrance survey
Land use survey
Frontage survey

## Slide 57
Urban Data Input Tool
Entrance tool
Land use tool
Frontage tool

## Slide 58
Urban Data Input Tool Frontage tool
Data categories
Create New Frontage layer
Using buildings/block dataset
Without using building/block dataset
Frontage Category
Selected feature data
Update buttons
Hide lines with no data

## Slide 59
Urban Data Input Tool Frontage tool

## Slide 60
Urban Data Input Tool Entrance tool
Data categories
Create New Entrance layer
Entrance Category
Selected feature data
Update buttons

## Slide 61
Urban Data Input Tool Entrance tool

## Slide 62
Urban Data Input Tool Land use tool
Data categories
Create New Land use layer
Land use Category
Selected feature data
Update buttons
Building data/ description

## Slide 63
Urban Data Input Tool Land use tool

## Slide 64
Connecting and analysing the various results
Catchment Analyser: calculating service/catchment areas from different locations (e.g. public transport nodes) along the road centreline network.
Task 4

## Slide 65
This plugin takes a line-based network and point-based origin layer and calculated the distance from each segment within a given distance or list of distances to each of the origins. The tool outputs the catchment as lines and as a concave hull polygon layer. Credit for the concave hull functionality goes to the algorithm described by Adriano Moreira and Maribel Yasmina Santos.
Catchment Analyser

## Slide 66
Network layer Choose the line-based vector layer that comprises a topological network you want to analyse. (projected CRS only!!)
Custom cost By default the tool will generate catchments based on the length of the network segments. If checked the tool will apply a weight based on the column selected.
Origin layer Choose the point-based vector layer containing the origins from which catchment will be calculated.
Origin Names By default the origin names will be based on the feature ids. If checked the tool will run the catchment analysis based on the column selected.
Cost Bands This sets the radius for the catchment analysis. For example, 400,800,1200,2000.
Network tolerance This is a tolerance for disconnected network. For example, it will connect lines that are within 1m by default.
Polygon tolerance The Catchment Analyser tool creates concave hull polygons from a specific origin. The polygon tolerance defines the level of 'concaveness' of the catchment. The lower the value, the more concave and the higher the value the more convex.
Catchment network The tool provides a catchment network output based on the original network layer with cost information on every origin. If checked the tool will generate the network as a temporary layer or as a shapefile using the browse button.
Catchment polygon The tool provides a catchment polygon output for each origin and each specified cost. If checked the tool will generate the polygons as a temporary layer or as a shapefile using the browse button.
Catchment Analyser

## Slide 67
Connecting and analysing the various results
Gate Transformer: preparing pedestrian counts
Connecting the centrality measures with pedestrian counts
Connecting the catchment results with pedestrian counts
Statistical analysis of two variables
Task 4

## Slide 68
Gate Transformer is a plugin to modify the geometry of gates used in space syntax movement observations. Gates are usually drawn perpendicular to the axial line, with varying lengths. For presentation of movement observations the typical output is a map showing lines along the axial lines to indicate the movement direction. The gates should all be rotated 90degrees and have the same length.
Gate Transformer

## Slide 69
Gates layer Choose the line-based gate layer from the drop-down menu that you want to transform
Rotate Line (degree) Define the angle in degrees for rotating the selected gates
Resize Line (metre) Define the length in metres for resizing the selected gates
Rescale Line (multiple) Define the multiple in ratio for rescaling the selected gates
Transform Pressing the transform button will activate the analysis for the selected transformation
Close Pressing close will close and terminate the Gate Transformer
Rotate Line
Resize Line
Rescale Line
Gate Transformer

## Slide 70
QGIS methods for space syntax research
Road centre lines: an approximation of segment maps?
Road centre lines: which model is more appropriate?
Connecting and analysing other data layers
Analysis with R and other statistics packages
Open to questions from the participants
Questions and Discussion

## Slide 71
Road centre lines: an approximation of segment maps?
Questions and Discussion

## Slide 72
Road centre lines: which model is more appropriate?
Questions and Discussion

## Slide 73
Thank you!
SST repository:
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit
SST mailing list:
https://www.jiscmail.ac.uk/cgi-bin/webadmin?A0=SPACESYNTAX-TOOLKIT
Space syntax mailing list:
https://www.jiscmail.ac.uk/cgi-bin/webadmin?A0=SPACESYNTAX