## Slide 1
Space Syntax Toolkit for QGIS Introduction and recent developments
Jorge Gil
Ioanna Kolovou
Abhimanyu Acharya
Stephen Law
Laurens Versluis
Space Syntax Laboratory - UCL
Space Syntax Limited - Open Digital Works
11th International Space Syntax Symposium
Fundação Calouste Gulbenkian, Lisbon
3rd July 2017

## Slide 2
Introduction
Who we are
Jorge Gil MSc, PhD
Researcher UCL, Chalmers, TU Delft
Open Source GIS consultant and developer
Author ‘Space Syntax Toolkit’ for QGIS (2013 - )
Author ‘Confeego’ for MapInfo (2004 - 09)
Abhimanyu Acharya MSc?
Associate, Space Syntax Ltd
Ioanna Kolovou MRes
Consultant, Space Syntax Ltd
Stephen Law MSc, PhD
Researcher Turing Institute, UCL
Associate, Space Syntax Ltd

## Slide 3
Introduction

## Slide 4
Introduction
Who are you?
Name and affiliation

## Slide 5
Introduction
Who are you?
Name and affiliation
 | Yes / Some | No
space syntax | 3 | 0
depthmapX | 2 | 1
QGIS | 1 | 2
GIS | 2 | 1
Note: based on 3 participant’s responses…

## Slide 6
Introduction
Objectives
Learn how to use the 'Space Syntax Toolkit' (SST) for QGIS
Learn about its latest features and tools
Explore various space syntax analysis workflows in QGIS
Main objective is not to…
Learn about space syntax theory and methods
Learn about the depthmapX software
Learn about specific space syntax applications in research

## Slide 7
Requirements
Participants must bring their own laptops in order to carry out the practical exercises, with the necessary software pre-installed:
QGIS 2.14 LTR (or higher):
http://qgis.org/en/site/forusers/download.html
depthmapXnet 0.35:
http://archtech.gr/varoudis/depthmapX/?dir=depthmapXnet
Space Syntax Toolkit:
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit/wiki/Installation
Introduction

## Slide 8
Programme
09:30 Introduction to the workshop
09:45 Overview of space syntax and the SST project
10:00 Task 1: Preparing and analysing axial models
11:00 Break
11:45 Task 2: Preparing and analysing road centre line models
12:30 Visualisation and discussion of the results
13:00 Lunch Break
14:00 Task 3: Preparing other urban data layers
15:00 Task 4: Connecting and analysing the various results
16:00 Discussion on QGIS methods for space syntax research
16:30 Close
Introduction

## Slide 9
Space syntax theory and methods
and the SST project
Overview

## Slide 10
Installation and Settings

## Slide 11
New Set of Plugins
Catchment Analyser
UrbanDataInput Tool
Road network cleaner
Gate Transformer

## Slide 12
Demo Flowchart
RCL Topology Cleaning
Processing algorithm: simplify geometries
Space Syntax Analysis
Catchment Analyser
Visualisation
Gate Transformer/movement correlation
Urban data input
Integrated Urban Model

## Slide 13
Preparing and analysing axial models
Task 1

## Slide 15
Preparing and analysing road centre line models
Task 2

## Slide 16
This plugin corrects topological errors of Road-centre-line (RCL) maps. This is a necessary step before performing space syntax analysis to any network.
Road network cleaner

## Slide 17
Road network cleaner
Removes invalid geometries
Removes point geometries
Breaks multi-part geometries
Breaks geometries at self intersection (1), at shared vertices (2) and where they touch endpoints of other lines (3).
Merges lines between intersections
Removes duplicate and overlapping (1) geometries, closed polylines that do not connect to any other line (2) and isolated lines (3).
Geometry
Topology
x
x
x

## Slide 18
Road network cleaner
Input layer Choose RCL map to clean. The input can be any QGIS layer.
Snap endpoints The user can specify a decimal precision of the coordinates
Output layers The user can choose between a memory QGIS layer a shapefile or a PostGIS database layer.
Load error layer The errors that have been corrected by the plugin can be loaded as a memory layer.
Load unlinks layer There is an option to create a memory unlinks layer where the lines of the input layer cross. However, unlinks should be verified by the user as RCL may represent differently unlinked lines.
Info See which topological errors are corrected.
Run Pressing run will perform the cleaning of the selected map
Cancel Pressing close will close and terminate the Road network cleaner

## Slide 19
Road network cleaner
Shapefile
Save output file: Select the location you wish to save the cleaned shapefile.
PostGIS layer
Database Select the database where to save the cleaned layer
Schema Select the schema where to save the cleaned layer
Table name Specify the table name of the cleaned layer or leave it as default (‘cleaned’)

## Slide 20
Network cleaning
OpenStreetMap
input
OS Open Roads
input

## Slide 21
Network cleaning
OpenStreetMap
errors
OS Open Roads
errors

## Slide 22
Network cleaning
OpenStreetMap
output
OS Open Roads
output

## Slide 23
Network simplification
Source: https://www.researchgate.net/figure/260758647_fig6_Figure-6-Simplification-of-a-polygonal-curve-with-the-Douglas-Peucker-algorithm-A
Douglas-Peucker generalisation algorithm

## Slide 24
Network simplification
QGIS – Simplify geometries

## Slide 25
Network simplification
OpenStreetMap
OS Open Roads

## Slide 26
Network segmentation
QGIS – Explode lines

## Slide 27
Network analysis
SST
Map
Segment map or road centre line: Tick this option when you are analysing road centre line maps or axial maps already segmented.

## Slide 28
Network analysis

## Slide 30
Preparing other urban data layers
Task 3

## Slide 31
Urban Data Input Tool
Urban Data Input Tool is a plugin to ease aid the input of urban data like frontage type, entrance type and land use type as per Space Syntax Limited standards. The Space Syntax community is the key users for the plugin. The display styles and categories included are as per Space Syntax Limited Standards.

## Slide 32
Urban Data Input Tool
Entrance tool
Land use tool
Frontage tool

## Slide 33
Urban Data Input Tool Frontage tool
Data categories
Create New Frontage layer
Using buildings/block dataset
Without using building/block dataset
Frontage Category
Selected feature data
Update buttons
Hide lines with no data

## Slide 34
Urban Data Input Tool Frontage tool

## Slide 35
Urban Data Input Tool Entrance tool
Data categories
Create New Entrance layer
Entrance Category
Selected feature data
Update buttons

## Slide 36
Urban Data Input Tool Entrance tool

## Slide 37
Urban Data Input Tool Land use tool
Data categories
Create New Land use layer
Land use Category
Selected feature data
Update buttons
Building data/ description

## Slide 38
Urban Data Input Tool Land use tool

## Slide 39
Creating catchments
Task 4

## Slide 40
This plugin takes a line-based network and point-based origin layer and calculated the distance from each segment within a given distance or list of distances to each of the origins. The tool outputs the catchment as lines and as a concave hull polygon layer. Credit for the concave hull functionality goes to the algorithm described by Adriano Moreira and Maribel Yasmina Santos.
Catchment Analyser

## Slide 41
Network layer Choose the line-based vector layer that comprises a topological network you want to analyse. (projected CRS only!!)
Custom cost By default the tool will generate catchments based on the length of the network segments. If checked the tool will apply a weight based on the column selected.
Origin layer Choose the point-based vector layer containing the origins from which catchment will be calculated.
Origin Names By default the origin names will be based on the feature ids. If checked the tool will run the catchment analysis based on the column selected.
Cost Bands This sets the radius for the catchment analysis. For example, 400,800,1200,2000.
Network tolerance This is a tolerance for disconnected network. For example, it will connect lines that are within 1m by default.
Polygon tolerance The Catchment Analyser tool creates concave hull polygons from a specific origin. The polygon tolerance defines the level of 'concaveness' of the catchment. The lower the value, the more concave and the higher the value the more convex.
Catchment network The tool provides a catchment network output based on the original network layer with cost information on every origin. If checked the tool will generate the network as a temporary layer or as a shapefile using the browse button.
Catchment polygon The tool provides a catchment polygon output for each origin and each specified cost. If checked the tool will generate the polygons as a temporary layer or as a shapefile using the browse button.
Catchment Analyser

## Slide 42
Gate Transformer is a plugin to modify the geometry of gates used in space syntax movement observations. Gates are usually drawn perpendicular to the axial line, with varying lengths. For presentation of movement observations the typical output is a map showing lines along the axial lines to indicate the movement direction. The gates should all be rotated 90degrees and have the same length.
Gate Transformer

## Slide 43
Gates layer Choose the line-based gate layer from the drop-down menu that you want to transform
Rotate Line (degree) Define the angle in degrees for rotating the selected gates
Resize Line (metre) Define the length in metres for resizing the selected gates
Rescale Line (multiple) Define the multiple in ratio for rescaling the selected gates
Transform Pressing the transform button will activate the analysis for the selected transformation
Close Pressing close will close and terminate the Gate Transformer
Rotate Line
Resize Line
Rescale Line
Gate Transformer

## Slide 44
Connecting and analysing the various results
Task 5

## Slide 45
QGIS methods for space syntax research
Questions and Discussion

## Slide 46
Thank you!
SST repository:
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit
SST mailing list:
https://www.jiscmail.ac.uk/cgi-bin/webadmin?A0=SPACESYNTAX-TOOLKIT
Space Syntax limited repository:
https://github.com/spacesyntax
Space syntax mailing list:
https://www.jiscmail.ac.uk/cgi-bin/webadmin?A0=SPACESYNTAX