## Slide 1
Space Syntax Toolkit for QGIS Introduction and recent developments
Abhimanyu Acharya
Associate, Space Syntax Ltd.
Ioanna Kolovou
Senior consultant, Space Syntax Ltd.
Space Syntax Laboratory - UCL
Space Syntax Limited
Workshop 3
Space syntax and analytical design workshops
MSc, MRes Space Syntax: Architecture and Cities
UCL

## Slide 2
Introduction
Who we are
Jorge Gil MSc, PhD
Researcher UCL, Chalmers, TU Delft
Open Source GIS consultant and developer
Author ‘Space Syntax Toolkit’ for QGIS (2013 - )
Author ‘Confeego’ for MapInfo (2004 - 09)
Stephen Law MSc
Researcher, Turing Institute, UCL
Associate, Space Syntax Limited
Ioanna Kolovou MRes
Senior Consultant, Space Syntax Limited
Abhimanyu Acharya MSc
Associate, Space Syntax Limited

## Slide 3
Introduction

## Slide 4
Introduction
Objectives
Learn how to use the 'Space Syntax Toolkit' (SST) for standard Space syntax axial and segment analysis in QGIS
Learn about data input methods

## Slide 5
Requirements
Participants must bring their own laptops in order to carry out the exercises, with the necessary software pre-installed:
QGIS 2.14 LTR (or higher):
http://qgis.org/en/site/forusers/download.html
depthmapXnet 0.35:
http://archtech.gr/varoudis/depthmapX/?dir=depthmapXnet
Space Syntax Toolkit:
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit/wiki/Installation
Introduction

## Slide 6
Programme
Introduction to SSXToolkit
Task 1a - Model preparation & verification
Task 1b – Model processing & visualisation
Task 2 – Data input
Introduction

## Slide 7
Space syntax theory and the SST project
Overview of relevant space syntax concepts
Overview of the SST project
SST installation in QGIS and downloading the sample data set
Overview

## Slide 8
The SST Project

## Slide 9
The SST Project

## Slide 10
Original tools: SST version 0.1.x
Graph Analysis
Attribute Explorer

## Slide 11
New Set of tools: SST version 0.2.0
Catchment Analyser
Urban Data Input Tool
Road network cleaner
Gate Transformer

## Slide 12
Demo Workflow
RCL Topology Cleaning
Processing algorithm: simplify geometries
Space Syntax Analysis
Catchment Analyser
Visualisation
Gate Transformer/movement correlation
Urban data input
Integrated Urban Model
Axial Map Verification
Unlinks Verification

## Slide 13
SST Installation

## Slide 14
SST Installation

## Slide 15
Preparing and analysing axial models
Model preparation: making axial and unlinks maps
Model verification: verifying the axial and unlinks maps
Model analysis: Axial and segment analysis of the axial model
Visualising the results
Task 1

## Slide 16
Drawing an axial map (use a projected CRS!)
Model preparation: making axial and unlinks maps

## Slide 17
Drawing an unlinks map
Model preparation: making axial and unlinks maps

## Slide 18
Load the layers in the Graph Analysis Tool
Model verification: verifying the axial and unlinks maps

## Slide 19
Verification is done on the two layers combined
Model verification: verifying the axial and unlinks maps

## Slide 20
Axial map errors
Model verification: verifying the axial and unlinks maps
Polyline
Duplicate
Undershoot
(short line)
Orphan
Unlinked orphan
Island
Small
Coinciding points
a)
b)
c)
d)
e)
f)

## Slide 21
Correcting the axial map
Model verification: verifying the axial and unlinks maps

## Slide 22
Correcting the axial map
Model verification: verifying the axial and unlinks maps

## Slide 23
Representing unlinks
Model verification: verifying the axial and unlinks maps

## Slide 24
Unlink errors
Model verification: verifying the axial and unlinks maps
Feature errors:
More than 2 lines
Single line
No lines
Attribute error:
No line id
Same line id
Unmatched line id
1
2
3

## Slide 25
Correcting the unlinks map
Model verification: verifying the axial and unlinks maps

## Slide 26
Axial model verification workflow
It’s an iterative process that stops when the verification of axial map and unlinks returns no errors.
Verify and fix axial lines
Update unlinks ids
Verify and fix unlinks
Verify and fix axial lines
Verify and fix unlinks
Update unlink ids
Verify and fix axial lines
…
Model verification: verifying the axial and unlinks maps

## Slide 27
DepthmapX remote axial analysis settings
Model analysis: Axial analysis of the axial model

## Slide 28
DepthmapX remote segment analysis settings
Model analysis: Segment analysis of the axial model

## Slide 29
Results report and postprocessing the results
Model analysis

## Slide 30
Loading analysis results in Attributes Explorer Tool
Visualising the results

## Slide 31
Changing colour range
Visualisation and discussion of the results

## Slide 32
Changing intervals: 10 quantiles
Visualisation and discussion of the results

## Slide 33
Changing intervals: equal ranges with Choice
Visualisation and discussion of the results

## Slide 34
Changing intervals: 10 quantiles with Choice
Visualisation and discussion of the results

## Slide 35
Changing intervals: custom range with Choice
Visualisation and discussion of the results

## Slide 36
Normalisation of Space Syntax measures
Normalised angular choice
Normalised choice aims to solve the paradox that segregated designs add more total (and average) choice to the system than integrated ones. It divides total choice by total depth for each segment in the system. This adjusts choice values according to the depth of each segment in the system, since the more segregated is, the more its choice value with be reduced by being divided by a higher total depth number. This would seem to have the effect of measuring choice in a cost-benefit way.
Sources Hillier, B., Yang, T., Turner, A., (2012) Advancing depthmap to advance our understanding of cities. In: Greene, M and Reyes, J and Castro, A, (eds.) 8th International Space Syntax Symposium. Pontificia Universidad Catolica de Chile: Santiago, Chile.
Normalising least angle choice in Depthmap - and how it opens up new perspectives on the global and local analysis of city space
http://discovery.ucl.ac.uk/1389938/
NACH = logCH+1/logTD+3

## Slide 37
Normalised angular integration
Normalised angular integration aims to normalise angular total depth by comparing the system to the urban average.
Sources Hillier, B., Yang, T., Turner, A. (2012) Advancing DepthMap to advance our understanding of cities: comparing streets and cities, and streets to cities. In: Greene, M and Reyes, J and Castro, A, (eds.) 8th International Space Syntax Symposium. Pontificia Universidad Catolica de Chile: Santiago, Chile.
NAIN = NC^1.2/TD
Normalising least angle choice in Depthmap - and how it opens up new perspectives on the global and local analysis of city space
http://discovery.ucl.ac.uk/1389938/
Normalisation of Space Syntax measures

## Slide 39
Preparing other urban data layers
Urban Data Input Tool: recoding frontages, entrances and land use surveys
Creating the data layer
Drawing new features
Updating features
Viewing the attributes
Task 2

## Slide 40
Urban Data Input Tool
Urban Data Input Tool is a plugin to ease aid the input of urban data like frontage type, entrance type and land use type as per Space Syntax Limited standards. The Space Syntax community is the key users for the plugin. The display styles and categories included are as per Space Syntax Limited Standards.

## Slide 41
Urban Data Input Tool
Entrance survey
Land use survey
Frontage survey

## Slide 42
Urban Data Input Tool
Entrance tool
Land use tool
Frontage tool

## Slide 43
Urban Data Input Tool Frontage tool
Data categories
Create New Frontage layer
Using buildings/block dataset
Without using building/block dataset
Frontage Category
Selected feature data
Update buttons
Hide lines with no data

## Slide 44
Urban Data Input Tool Frontage tool

## Slide 45
Urban Data Input Tool Entrance tool
Data categories
Create New Entrance layer
Entrance Category
Selected feature data
Update buttons

## Slide 46
Urban Data Input Tool Entrance tool

## Slide 47
Urban Data Input Tool Land use tool
Data categories
Create New Land use layer
Land use Category
Selected feature data
Update buttons
Building data/ description

## Slide 48
Urban Data Input Tool Land use tool

## Slide 49
Preparing other pedestrian data layers
Creating the data layer
Drawing new features
Updating features
Viewing the attributes
Task 3

## Slide 50
Pedestrian Data Input - Pedestrian traces and snapshots

## Slide 51
Pedestrian Data Input - Pedestrian snapshots

## Slide 52
Pedestrian Data Input - Pedestrian traces
Cromwell Road Entrance
Mammals
Earth Galleries
38%
3%
3%
Dinosaurs
6%
Waterhouse Gallery
(Temporary)
To upper levels
1%
Jerwood Gallery
(Temporary)
1%
Creepy Crawlies
2%
Ecology
3%
Café
2%
Shop
2%
Restaurant
2%
Human Biology
1%
Darwin Centre
1%
Ground
7%
Central Hall

## Slide 53
SST Github repository
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit

## Slide 54
SST Issues
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit/issues

## Slide 55
SST Wiki
https://github.com/SpaceGroupUCL/qgisSpaceSyntaxToolkit/wiki

## Slide 56
Thank you!
SST mailing list:
https://www.jiscmail.ac.uk/cgi-bin/webadmin?A0=SPACESYNTAX-TOOLKIT
Space syntax mailing list:
https://www.jiscmail.ac.uk/cgi-bin/webadmin?A0=SPACESYNTAX